## Slide 1
MONITORING PERACETIC ACID

## Slide 2: Presentation to National Chicken Council November 7, 2018

## Slide 3: Presented by Interscan Corporation

## Slide 4: Peracetic Acid
aka Peroxyacetic Acid
aka Ethaneperoxoic Acid
aka PAA

## Slide 5: History

## Slide 6
PAA first registered in the U.S. as a pesticide for use as a disinfectant, sanitizer, and sterilant in 1985.
FDA approved for direct contact with food, food processing equipment and utensils, and other food contact surfaces (21 C.F.R. § 178.1010,
April 1, 2011

## Slide 7: Occupational Health Considerations

## Slide 8
OSHA—No PEL, but other standards do exist. Thus, agency has issued Rapid Response letters and citations under the General Duty Clause, for what it deems to be high exposures.
Cal/OSHA—Proposed: 0.15 ppm (8 hr TWA); 0.4 ppm (15 min STEL)
NIOSH—No REL, but proposed IDLH of 0.64 ppm
ACGIH TLV—0.4 ppm as a 15-min STEL

## Slide 9: Chemical Properties

## Slide 10
Anhydrous peracetic acid explodes violently upon heating
PAA sanitizers created by combining aqueous acetic acid and hydrogen peroxide
Equilibrates to solution containing peracetic acid, acetic acid, and hydrogen peroxide
Breaks down rapidly in air

## Slide 11
Gas Detection Challenges

## Slide 12
PAA unstable in air, so calibration standard must be generated on-the-fly
This stream must then be analyzed using wet chemistry
Now, you have a standardized calibration source;
good for two hours
DPD (N, N-diethyl-p-phenylenediamine) method: PAA oxidizes
iodide to iodine; iodine oxidizes DPD forming pink product

## Slide 13
True field calibration is impractical— but a good PAA bump test can be supplied
A suitable PAA solution, activated with a bubbler generates a
gas stream. User refers to calibration chart, by temperature
and flow rate.
Pre-calibrated sensors are delivered to user on a scheduled
basis. Nothing to send back to factory.
Best solution is our SENSOR EXPRESS® program

## Slide 14
Products

## Slide 15
Portable Survey Monitors
All featuring reliable sample-draw pump

## Slide 17
Single Point
Continuous Monitoring
Systems
Designed for heavy-duty industrial applications;
Sample-draw pump

## Slide 19
Multi-Point
Continuous Monitoring
Systems
Featuring the best in
factory automation

## Slide 23
Arc-Max®
Data Acquisition / Logging / Archiving / Reporting System

## Slide 24
Features Shift Reports, supporting up to four shifts, which can overlap
Shift Minimum and Maximum values
Alarm indication and alarm logs
Instantaneous reading at all points

## Slide 25
8 hour time-weighted average—all points
Live and historic trending
The four highest 15-minute average exposures that occurred during the shift (STEL)
Web-based application coming soon

## Slide 29
Interscan...
Solving gas detection
problems since 1975
Well-known for
getting it done in the
toughest applications

## Slide 30
Special thanks
to
Ashley Peterson